## Slide 1: GreenBag: Energy-efficient Bandwidth Aggregation for Real-time Streaming in Heterogeneous Mobile Wireless Networks
Student: Bui, Hoang Duc
Advisor: Professor Shin, Insik

## Slide 2: Motivation
Mobile multimedia streaming is very popular today
  Real-time multimedia streaming traffic will take up to 66% of global mobile data traffic by 2017, up from 51% in 2012 [Cisco Systems Forecast]
High quality video streaming needs high bandwidth
  Streaming ultra-HD 4K videos requires around 19Mbps bandwidth [Youtube]
  High definition cameras on modern smartphones are capable of recording 1080p full-HD videos at 17-24Mbps bit rates

## Slide 3: Bandwidth aggregation on mobile devices - Opportunity
Increasing usable bandwidth by bandwidth aggregation: create one logical link via two physical links
  Common mobile phones are equipped with at least two network interfaces, 3G/LTE and WiFi
  LTE provides high bandwidth comparable to WiFi
Notes: Fortunately

## Slide 4: Bandwidth aggregation
Bandwidth aggregation needs to divide the file downloading into the two different interfaces
  Divide the file into small segments and assign each segment to one of the links for downloading

## Slide 5: Bandwidth aggregation
Bandwidth aggregation needs to divide the file downloading into the two different interfaces
  Divide the file into small segments and assign each segment to one of the links for downloading
File

## Slide 6: Bandwidth aggregation
Bandwidth aggregation needs to divide the file downloading into the two different interfaces
  Divide the file into small segments and assign each segment to one of the links for downloading
File

## Slide 7: Bandwidth aggregation
Bandwidth aggregation needs to divide the file downloading into the two different interfaces
  Divide the file into small segments and assign each segment to one of the links for downloading
LTE
WiFi
WiFi
LTE
LTE
WiFi
LTE
WiFi
WiFi
WiFi
File

## Slide 8: Bandwidth aggregation
Bandwidth aggregation needs to divide the file downloading into the two different interfaces
  Divide the file into small segments and assign each segment to one of the links for downloading
Two basic problems must be solved
  Segment size decision
  Segment channel assignment
LTE
WiFi
WiFi
LTE
LTE
WiFi
LTE
WiFi
WiFi
WiFi
File

## Slide 9: Bandwidth aggregation
Bandwidth aggregation needs to divide the file downloading into the two different interfaces
  Divide the file into small segments and assign each segment to one of the links for downloading
Two basic problems must be solved
  Segment size decision
  Segment channel assignment
Important issue: out-of-order delivery
  We cannot use out-of-order segments for playing back which requires in-order data
LTE
WiFi
WiFi
LTE
LTE
WiFi
LTE
WiFi
WiFi
WiFi
Out-of-order segment
Downloading in progress
File
Downloaded portion

## Slide 10: Bandwidth aggregation on mobile devices – Requirements
Strict energy saving requirement
  Mobile devices are powered by batteries
  The use of multiple network interfaces can introduce a significant energy usage
  LTE and WiFi have different power management
Ease of deployment
  A widely applicable technique should require no change to the Internet infrastructure
Notes: However

## Slide 11: Goal
Address the two basic problems in order to support the QoS requirements of real-time video streaming in the most energy-efficient way
  Segment size decision
  Segment channel assignment
  In this thesis, we consider only on-demand video streaming in which the video file size is known
LTE
WiFi
WiFi
LTE
LTE
WiFi
LTE
WiFi
WiFi
WiFi

## Slide 12: Problem Formulation
Considering QoS satisfaction more important than energy saving, we formulate the multi-objective optimization problem as a lexicographic optimization
  Problem #1: Decide the size and channel assignment of each segment which minimize playback time P subject to throughput of LTE and throughput of WiFi
  Problem #2: Decide the size and channel assignment of each segment which minimize energy consumption E subject to throughput of LTE and WiFi, and , where is the minimum playback time derived in optimization #1

## Slide 13: Bandwidth aggregation on mobile devices – Challenges
Link heterogeneity
  Out-of-order packet delivery
Bandwidth fluctuation
  Accurate prediction of network condition is not possible
Places
LTE bandwidth fluctuation
Bandwidth heterogeneity in different places
Notes: However

## Slide 14: Approach: Multi-link Data Streaming Scheme
Divide a file into segments, then divide each segment further into two subsegments, and assign each subsegment into one of the two interfaces for downloading
In-order Data
Notes:   Use LTE and WiFi in a smart way so that we achieve the minimum video interruption time at the minimum energy consumption

## Slide 15: GreenBag architecture
GreenBag is a middleware which provides energy-efficient multi-link data streaming services
  GreenBag’s role is as a proxy between video player and server
Download Planner
Download Engine
Server
Video Player
HTTP
Engine
Buffer
LTE
WiFi
GreenBag

## Slide 16: GreenBag architecture
GreenBag is a middleware which provides energy-efficient multi-link data streaming services
  GreenBag’s role is as a proxy between video player and server
Download Planner
Download Engine
Server
Video Player
HTTP
Engine
Buffer
LTE
WiFi
Segment Manager
Recovery Decision Maker
Goodput Predictor
Energy Model
Energy-aware
Link Mode Chooser
Medium Load Balancer
Video Player State Monitor
GreenBag

## Slide 17: Components of Download Planner (1/5)
Segment Manager
  Determine the next segment size when a segment completes
    It uses a fixed segment size in typical cases
    Overhead of requesting a segment is small because of the use of HTTP pipelining
Download Planner
Segment Manager
Recovery Decision Maker
Goodput Predictor
Energy Model
Energy-aware
Link Mode Chooser
Medium Load Balancer
Video Player State Monitor
Notes:   Given a link is finishing while the other link is still downloading its subsegment, the subsegment sizes are computed as
    () and () are the subsegment size and goodput link () in the next segment of size , respectively
    is the size of unfinished portions of both links, mainly of link
  Given a link 𝑎 is finishing while the other link 𝑏 is still downloading its subsegment, the subsegment sizes are computed as
  {█(𝑍_𝑎=𝐺_𝑎/(𝐺_𝑎+𝐺_𝑏 )∙(𝑍+𝑍_𝑢 )" " @𝑍_𝑏=𝑍+𝑍_𝑢−𝑍_𝑎 )┤
    𝑍_𝑎 (𝑍_𝑏) and 𝐺_𝑎 (𝐺_𝑏) are the subsegment size and goodput link 𝑎 (𝑏) in the next segment of size 𝑍, respectively
    𝑍_𝑢is the size of unfinished portions of both links, mainly of link 𝑏

## Slide 18: Components of Download Planner (2/5)
Medium Load Balancer
Determine the subsegment sizes and links’ assignment in the next segment
  Basing on unfinished portion size, next segment size, and estimation of current goodput
    Reduce out-of-order delivery
  Both interfaces would finish at the same time
  The faster link would download the earlier subsegment
Require good estimation of current goodput
Download Planner
Segment Manager
Recovery Decision Maker
Goodput Predictor
Energy Model
Energy-aware
Link Mode Chooser
Medium Load Balancer
Video Player State Monitor
Notes:   Given a link is finishing while the other link is still downloading its subsegment, the subsegment sizes are computed as
    () and () are the subsegment size and goodput link () in the next segment of size , respectively
    is the size of unfinished portions of both links, mainly of link
  The size of a subsegment assigned to link is proportional to the link’s goodput , and the sum of the unfinished portion of both link and next segment size
  Given a link 𝑎 is finishing while the other link 𝑏 is still downloading its subsegment, the subsegment sizes are computed as
  {█(𝑍_𝑎=𝐺_𝑎/(𝐺_𝑎+𝐺_𝑏 )∙(𝑍+𝑍_𝑢 )" " @𝑍_𝑏=𝑍+𝑍_𝑢−𝑍_𝑎 )┤
    𝑍_𝑎 (𝑍_𝑏) and 𝐺_𝑎 (𝐺_𝑏) are the subsegment size and goodput link 𝑎 (𝑏) in the next segment of size 𝑍, respectively
    𝑍_𝑢is the size of unfinished portions of both links, mainly of link 𝑏
  The size of a subsegment assigned to link 𝑎 is proportional to the link’s goodput 𝐺_𝑎, and the sum (𝑍_𝑢+𝑍) of the unfinished portion of both link 𝑍_𝑢 and next segment size 𝑍

## Slide 19: Components of Download Planner (3/5)
Recovery Decision Maker
Handle the case when goodput estimation is wrong
Replan the downloading again
  When GreenBag made poor decisions on load balancing due to fast fluctuation of network bandwidth, such as a drop of WiFi bandwidth
Download Planner
Segment Manager
Recovery Decision Maker
Goodput Predictor
Energy Model
Energy-aware
Link Mode Chooser
Medium Load Balancer
Video Player State Monitor
Notes:   Recover only when bottleneck subsegment is significantly lagging in the way that there is a high chance to miss a QoS deadline and cause a video playback interruption
    Avoid both QoS violation and overhead of recovery
  where
    is the time available for continuing playing back without interruption
    is the time required to finish the bottleneck subsegment
    is a weighted value
  Condition for recovery is when there is insufficient time available for continue playing back without interruption
{█(𝑍_𝑎=𝐺_𝑎/(𝐺_𝑎+𝐺_𝑏 )∙(𝑍+𝑍_𝑢 )" " @𝑍_𝑏=𝑍+𝑍_𝑢−𝑍_𝑎 )┤

## Slide 20: Components of Download Planner (4/5)
Energy-aware Link-mode Chooser
Download Planner
Segment Manager
Recovery Decision Maker
Goodput Predictor
Energy Model
Energy-aware
Link Mode Chooser
Medium Load Balancer
Video Player State Monitor
Notes:   LTE will demote to IDLE state after if is idle in more than
{█(𝑍_𝑎=𝐺_𝑎/(𝐺_𝑎+𝐺_𝑏 )∙(𝑍+𝑍_𝑢 )" " @𝑍_𝑏=𝑍+𝑍_𝑢−𝑍_𝑎 )┤

## Slide 21: LTE power management
LTE power management has 3 states: ACTIVE, TAIL, and IDLE
  LTE interface in TAIL state has high power consumption, about half of the power in ACTIVE state
  The TAIL state timeout is long (11.2 seconds)
    Suggests to keep LTE idle long enough until LTE interface demotes to IDLE state which consumes almost no energy
ACTIVE
IDLE
TAIL
any data
traffic
TAIL state timeout expires
any data
traffic
no data
traffic
(a) LTE power states
(b) LTE power trace
IDLE
ACTIVE
TAIL

## Slide 22: Components of Download Planner (4/5)
Energy-aware Link-mode Chooser
Save energy by keeping LTE idle in long period (longer than )
  Avoid irregular data transfer over LTE which prevents LTE to enter IDLE state
Choose the link mode that consumes the least energy to download the remaining portion of the file without incurring any playback interruption
  Three link modes: Dual-link, LTE-only, and WiFi-only
Download Planner
Segment Manager
Recovery Decision Maker
Goodput Predictor
Energy Model
Energy-aware
Link Mode Chooser
Medium Load Balancer
Video Player State Monitor
Notes:   LTE will demote to IDLE state after if is idle in more than
{█(𝑍_𝑎=𝐺_𝑎/(𝐺_𝑎+𝐺_𝑏 )∙(𝑍+𝑍_𝑢 )" " @𝑍_𝑏=𝑍+𝑍_𝑢−𝑍_𝑎 )┤

## Slide 23: Components of Download Planner (5/5)
Goodput Predictor
  Predict goodput of each link in the remaining portion of the file using an exponential weighted moving average (EWMA) predictor
Video Player State Monitor
  Monitor the video player’s current state and position
Download Planner
Segment Manager
Recovery Decision Maker
Goodput Predictor
Energy Model
Energy-aware
Link Mode Chooser
Medium Load Balancer
Video Player State Monitor
Notes: {█(𝑍_𝑎=𝐺_𝑎/(𝐺_𝑎+𝐺_𝑏 )∙(𝑍+𝑍_𝑢 )" " @𝑍_𝑏=𝑍+𝑍_𝑢−𝑍_𝑎 )┤

## Slide 24: Download Planner - Decision Making
Typically, GreenBag makes the following decisions to download further when a link is going to finish its subsegment
  Decide to recover or not, if not
    Decide the next segment size
    Choose the most energy-efficient link mode
    Decide the subsegment sizes of the two links in the next segment
Download Planner
Segment Manager
Recovery Decision Maker
Goodput Predictor
Energy Model
Energy-aware
Link Mode Chooser
Medium Load Balancer
Video Player State Monitor
Notes: {█(𝑍_𝑎=𝐺_𝑎/(𝐺_𝑎+𝐺_𝑏 )∙(𝑍+𝑍_𝑢 )" " @𝑍_𝑏=𝑍+𝑍_𝑢−𝑍_𝑎 )┤

## Slide 25: Evaluation
Evaluation in real-world networks
Evaluation in emulated environment

## Slide 26: Evaluation in real-world networks Experiment Setup (1/2)
Compare 4 configurations (GB-E, GB-P, LTE-only, and WiFi-only) in 3 scenarios (Stationary #1, Stationary #2, and Mobile) in terms of 2 performance metrics
Two performance metrics
  Playback time
  Energy consumption
Four configurations
  GB-E: GreenBag-Energy mode, supports QoS while saving energy
  GB-P: GreenBag-Performance mode, maximizes throughput without saving energy
  LTE-only (WiFi-only): video streaming using only LTE (WiFi)
Notes:   Because of randomness of real-world environments, we did experiments 3 times for each pair of (configuration, scenario) and then derived average values

## Slide 27: Evaluation in real-world networks Experiment Setup (2/2)
Compare the 4 configurations (GB-E, GB-P, LTE-only, and WiFi-only) in 3 scenarios (Stationary #1, Stationary #2, and Mobile)
Three scenarios
    Stationary #1: Bandwidth of LTE is always greater than of WiFi
    Stationary #2: Bandwidth of LTE is always smaller than of WiFi
    Mobile: WiFi bandwidth fluctuates fast and has a drop due to user mobility
 | Stationary #1 | Stationary #2 | Mobile
Average LTE bandwidth (Mbps) | 5.14 | 4.12 | 4.73
Average WiFi bandwidth (Mbps) | 3.85 | 5.00 | 4.94
Total average bandwidth (Mbps) | 8.99 | 9.12 | 9.67
  Experimented video has 6.1Mbps average bit rate, and is 117 seconds long
Notes:   Because of randomness of real-world environments, we did experiments 3 times for each pair of (configuration, scenario) and then derived average values

## Slide 28: Performance of GreenBag in real-world experiments
GreenBag minimizes video interruption time
GB-E not only minimizes video interruption time but also consumes 14-25% less energy than GB-P

## Slide 29: Demonstration Playback time minimization
PlayTime.mp4
Please visit the following website for the video file http://cps.kaist.ac.kr/greenbag/

## Slide 30: Demonstration Energy Saving
EnergyConsumption.mp4
Please visit the following website for the video file http://cps.kaist.ac.kr/greenbag/
Notes: External power monitor tool

## Slide 31: Evaluation in Emulated environment
Experiment setup
  Emulated network
    A client, a server, and an intermediate node equipped with network emulator tools
  Emulated player
    Implementation of the video player model
Evaluate four aspects of GreenBag
  Segment size overhead
  Effectiveness of adaptive load balancing
  Effectiveness of recovery mechanism
  Effectiveness of energy-aware link mode switching

## Slide 32: Video Player Model
The video player is modeled as a queue in front of the video decoder
  Arrived data:
  Decoded data:
  Buffered data:
Video playback starts when data in the buffer is sufficient:
  B is called lower threshold
Video player pauses when buffered data decreases to zero
A(t)
X(t)
B
D(t)
Video
Decoder
Data Source
Video Buffer
A(t)
D(t)
Time
Data size
B
B
t0
t1
t2
t3
t4
L
X(t)
k-th
bit

## Slide 33: Segment size overhead
Optimal segment sizes are independent of bandwidth heterogeneity and video bit rates
  Small segment size imposes more overhead in requesting every new segment
  Large segment size increases out-of-order data delivery
(b) Overhead in different video bit rates
(a) Overhead in different link heterogeneity

## Slide 34: Effectiveness of adaptive load balancing
Bandwidth heterogeneity has little effect on the performance of the adaptive load balancing scheme, while affecting the fixed load balancing (1:1) significantly

## Slide 35: Effectiveness of recovery mechanism (1/2)
  Recovery mechanism avoids the long out-of-order data caused by bandwidth drops
  E.g. WiFi bandwidth can drop when the smartphone moves out of WiFi coverage

## Slide 36: Effectiveness of recovery mechanism (2/2)
Recovery mechanism keeps playback time minimum even in the presence of multiple of bandwidth drops

## Slide 37: Effectiveness of energy-aware link-mode switching
GB-E provides the same playback time with GB-P, while saving 2%-40% of energy consumption of GB-P

## Slide 38: Conclusion
The thesis has the following contributions
Formulate bandwidth aggregation for real-time video streaming as a lexicographic optimization
Design a multi-link data streaming middleware to support real-time delivery in the most energy-efficient way
Implement a prototype of GreenBag on Android-based mobile devices equipped with LTE and WiFi interfaces
  To the best of our knowledge, this is one of the first LTE-enabled prototypes which demonstrates the effectiveness of bandwidth aggregation for energy-efficient real-time delivery on mobile phones
Notes: + experiment + writing

## Slide 39: Acknowledgement
I would like to express my special thanks and appreciation to Kilho Lee, Sangeun Oh (Cyber-Physical Systems Lab), Doctor Hyojeong Shin (Mobile SW Platform Center), Doctor Honguk Woo, and Doctor Daehyun Ban (Samsung Electronics) for their great support and collaboration in the research

## Slide 40: Thank you
Questions and Answers

## Slide 41: Appendix Energy Models of LTE and WiFi
Transmission energy used to download Mbits with bandwidth Mbps is formulated as
  : power consumption; : time for downloading data
 | LTE | WiFi
 | 16.72 | 24.19
 | 2022.20 | 360.90
 | LTE | WiFi
 | 16.72 | 24.19
 | 2022.20 | 360.90
Energy consumption in TAIL state of LTE:
  Power consumption in TAIL state:
  is the duration in which LTE is in TAIL state
We ignore promotion, and data upload energy values, because they are too small